## Slide 1
Voice-Controlled IoT System with ESP32 & Relays
Smart Home Automation using Speech Recognition & Wi-Fi

## Slide 2
Introduction
IoT & Smart Control
IoT enables smart control of appliances via internet & automation
Project Integration
This project integrates ESP32 microcontroller, 2-channel relay, and Python voice recognition
Goal
Control lights/appliances using simple voice commands

## Slide 3
Core Components
ESP32
Wi-Fi enabled microcontroller at the heart of the system
Relay Module (2-channel)
Switches electrical appliances safely
Python SpeechRecognition
Listens to voice commands via microphone
Wi-Fi Communication
Python sends HTTP requests to ESP32

## Slide 4
ESP32 Role
Hosts a web server with /on and /off endpoints
Receives commands from Python script
Controls relay pins (GPIO 26 & 27)
Provides real-time feedback ("Lights ON" / "Lights OFF")

## Slide 5
Python Role
Voice Capture
Uses SpeechRecognition + PyAudio to capture voice input
Keyword Recognition
Recognizes keywords: "turn on", "light on", "turn off", "light off"
HTTP Request
Sends HTTP request to ESP32 server (/on or /off)
Voice-to-Action Bridge
Acts as the voice-to-action bridge between user and hardware

## Slide 6
Circuit Design
ESP32 connected to relay module
Relay channels wired to appliances (e.g., light bulb)
Common ground between ESP32 & relay
Wi-Fi ensures wireless control
All high-voltage wiring should be handled with proper insulation and safety precautions.

## Slide 7
Program Flow
Recognize
Convert speech to command
Receive
ESP32 web server handles it
Listen
Python captures voice input
Act
Relay toggles, appliance responds
Send
HTTP request dispatched

## Slide 8
Demo Dashboard
Serial Monitor
ESP32 IP address displayed on Serial Monitor output
Python Terminal
"You said: turn on → Lights ON" printed in terminal output
Live Appliance
Appliance switching ON/OFF in real time via relay

## Slide 9
Applications
Smart Home Automation
Control lights, fans, and appliances hands-free
Accessibility
Voice-controlled access for elderly and disabled users
Energy Management
IoT-based monitoring and energy efficiency
Scalable Expansion
Expandable to multiple relays & devices

## Slide 10
Benefits
Hands-Free Control
Operate appliances entirely through voice — no physical interaction needed
Low-Cost IoT Solution
Affordable components make smart automation accessible to everyone
Easy Integration
Works seamlessly with existing household appliances
Scalable
Designed to grow — add more relays and devices for smart homes & offices

## Slide 11
Summary
ESP32 + Relay
Hardware control
Python + SpeechRecognition
Voice interface
Wi-Fi
Seamless communication
Together
A simple, powerful voice-controlled IoT system